## Slide 1: Perfctr-Xen: A framework for Performance Counter Virtualization
Ruslan Nikolaev and Godmar Back
Virginia Polytechnic Institute
Blacksburg

## Slide 2: Overview
IaaS widely use virtual machine monitors
  Type 1 hypervisors: Xen, KVM, ESX …
Commonly used performance analysis tools (e.g., PAPI) cannot be used because existing VMM and guests do not provide necessary per-thread virtualization support for hardware event counters
Our contribution: Perfctr-Xen:
  Framework for performance counter virtualization
  Software-compatible with widely used perfctr library
  Techniques for collaboration of guest and hypervisor
Experimental validation

## Slide 3: Existing Performance Counter Virtualization Solutions
XenoProf
  Extension of Oprofile system-wide profiler
  Does not provide per-domain abstraction of hardware counter facilities (supports only 1 domain at a time)
VPMU driver
  Treats PMU registers like ordinary registers (saved/restored by VMM)
  Requires use of hardware assisted virtualization mode; support for limited number of architecture generations since VMM must contain architecture-specific code
  Not compatible with all architectures

## Slide 4: Perfctr-Xen
Kernel
Perfctr (Native)
Perfctr-Xen
PerfExplorer,
HPCToolkit, etc.
PAPI
Profilers
High-level performance counters
Low-level performance counters
PerfExplorer,
HPCToolkit, etc.
PAPI
Perfctr Lib
Perfctr Driver
Guest Kernel
Xen Hypervisor
Perfctr Guest Driver
Perfctr-Xen Driver
Perfctr Lib
Software
Compatible
Notes: Software engineering points: minor changes to perfctr lib, and complete reuse of architecture-dependent code in both guest kernel and hypervisor driver.

## Slide 5: Per-thread PMU Virtualization
Logical per-thread value includes only events incurred during the thread execution
Thread 0
Thread 1
Thread 0
Thread 1
Domain 0
Domain 1
Intradomain
Switch
Interdomain
Switch
Notes: Animation.
The diagram shows that intra-domain and inter-domain switches will affect how events must be counted. Since we have global counters, we have to take both type of context switches into account to correctly implement per-thread virtualization.

## Slide 6: Perfctr Library
6
Sumthread, Startthread
Sumthread, Startthread
Sumthread, Startthread
CPU1
Threads
Kernel level
Hardware
CPU2
User level
Perfctr library API or /dev/perfctr
Modes of operation
A-mode: an event count in some region of a program
I-mode: an interrupt after a certain number of events has occurred
Notes: User level threads have direct access! Low overhead! No system call required!
- Requires that kernel updates and exposes data structures to user level thread.
Read-only memory mapping to user level

## Slide 7: Perfctr: A-mode counters
Thread 0
Thread 1
t3
Sumthread
Phys(t2)-Startthread
Sumthread records accumulated event count
Kernel records physical value to Startthread = Phys(t1)
Kernel increments Sumthread = Sumthread + (Phys(t3) – Startthread)
t1
t2
Thread samples physical value Phys(t2), computes Logical value Logthread = Sumthread + (Phys(t2) – Startthread)
Phys(t3)-Startthread
Sumthread
Notes: Advantage: no expensive writes to PMU registers

## Slide 8: Perfctr: I-mode counters
PMU registers trigger interrupt on zero-overflow
Physical register initialized to negated sample period
Requires that physical value be saved & restored on each context switch
Compute logical accumulated value similar to a-mode
-5000
-1, 0
-5000
-1, 0
-5000
-1, 0
Events
Time
Notes: Change the order

## Slide 9: Perfctr-Xen: A-mode counters
Requires cooperation of guest kernel and hypervisor:
  Guest: maintains per-thread state: Sumthread, Startthread
  Hypervisor: a per-VCPU (Virtual CPU) state: Sumvcpu, Startvcpu
Guest kernel makes per-VCPU state available user threads
Sumthread, Startthread
Sumthread, Startthread
Sumvcpu, Startvcpu
Sumvcpu, Startvcpu
Sumthread, Startthread
CPU
VCPUs
Threads
Guest
Hypervisor
Hardware
Read-only mapping
Sumvcpu, Startvcpu
Notes: Talk about what a VCPU is (one sentence)
Introduce who updates which data structures

## Slide 10: Perfctr-Xen: A-mode counters
Thread 0
Thread 1
Thread 0
Thread 1
Domain 0
Domain 1
t1
t2
Sumthread
Sumvcpu
Phys(t2)-Startvcpu
Startvcpu = Phys(t1)

## Slide 11: Perfctr-Xen: A-mode counters
Thread 0
Thread 1
Thread 0
Thread 1
Domain 0
Domain 1
Hypervisor: Sumvcpu = 0, Startvcpu = Phys(t1)
Hypervisor: Sumvcpu = Sumvcpu + (Phys(t3) – Startvcpu)
Hypervisor: Startvcpu = Phys(t4)
t4
t5
Sumthread
Sumvcpu
Start*thread
Phys(t5)-Startvcpu
t1
t2
t3
Logthread = Sumthread + Sumvcpu + (Phys(t5) – Startvcpu) - Start*thread
Guest: Start*thread = Sumvcpu + (Phys(t2) – Startvcpu)
Hypercall:
Activate configuration
Sumvcpu ←0
Startvcpu ←Phys(t1)
Notes: Additional benefits: hypercall batching, hypercall is not always necessary, overhead can be accounted for

## Slide 12: Perfctr-Xen: I-mode counters
Suspension hypercall to increment Sumvcpu and sample Startvcpu
Resumption hypercall to restore per-VCPU values
Physical Counter Registers
Sumvcpu,
Startvcpu
Sumthread,
Startthread
Intra-domain context switch
Inter-domain context switch
Save
Save
Logthread = Sumvcpu + (Phys(t) – Startvcpu)
Restore
Restore

## Slide 13: Perfctr-Xen: Interrupt delivery
Hypervisor delivers overflow interrupts to guest via VIRQ_PERFCTR virtual interrupts
Upon receipt, guest kernel signals user thread
Virtual interrupts are delivered asynchronously (as soft interrupts)
Guest must ensure that overflow interrupt is delivered to correct thread by rechecking overflow status
  If thread causing overflow is suspended before virtual interrupt arrives at guest, mark as pending and deliver on next resume

## Slide 14: Experimental Results
Baseline: native execution
Exercise multiple VCPU/PCPU scenarios
Exercise multiple virtualization modes
  Paravirtualization
  Hardware-assisted virtualization (HVM)
  Hybrid mode (HVM + guest enhancement)
Correctness of implementation and accuracy of results
  Microbenchmarks for a-mode, PAPI test for i-mode
  Macrobenchmarks: SPEC CPU 2006
  Verify Profiling (HPCToolkit)

## Slide 15: Microbenchmarks
Each domain on 2 dedicated PCPUs; each thread on a dedicated VCPU.
Each domain on a dedicated PCPU; all threads in a domain on a shared VCPU.
All domains on a shared PCPU; all threads on a shared VCPU.
Random migration PCPUs and VCPUs

## Slide 16: SPEC CPU2006: L2 Cache Misses
Native mode
Fully-virtualized Dom1 and Dom2, each on a dedicated core
Fully-virtualized Dom1 and Dom2 on the same core
Paravirtualized Dom0 and Dom1, each on a dedicated core
Paravirtualized Dom0 and Dom1 on the same core

## Slide 17: SPEC CPU2006: L2 Cache References
Native mode
Fully-virtualized Dom1 and Dom2, each on a dedicated core
Fully-virtualized Dom1 and Dom2 on the same core
Paravirtualized Dom0 and Dom1, each on a dedicated core
Paravirtualized Dom0 and Dom1 on the same core

## Slide 18: Related Work
Performance counter support for VMM
  XenoProf [Menon 2005]
  Counter Virtualization for KVM [Du 2010, 2011]
  VTSS++ system [Bratanov 2009]
Performance counters in non-virtualized systems
perf_counter, Perfmon [Eranian 2006], Intel VTune, AMD Code Analyst
Higher-level libraries:
  PAPI [Browne 1999]

## Slide 19: Conclusion
PerfCtr-Xen
  Efficient and accurate per-thread virtualization of hardware event counters
  Supports all commonly used virtualization modes
  Plug-in Compatibility with PAPI, HPCToolkit, etc.
  Techniques extend to other Type I hypervisors and low-level virtualization libraries
Available at http://people.cs.vt.edu/~rnikola/
(LGPL license)